## Slide 1: Analysis of DTI Data
MP/NTP 651

## Slide 2: Diffusion Tensor Imaging
Basser et al. (1994)
Non-invasive imaging technique for estimating the diffusion properties of water in biological tissues
Highly sensitive to differences in tissue microstructure
Diffusion in white matter is anisotropic (varies with direction)
Orientation
of White Matter
T2W
Structure
Mean
Diffusion
(1/Density)
Fractional
Anisotropy
(‘White Matter’)
Parallel Diffusivity
(‘Axons’)
Perpendicular Diffusivity
(‘Myelin’)

## Slide 3
DTI Processing
DW images
Diffusion Tensor
Eigenvalues
MD
FA

## Slide 4: Diffusion Eigenvalues
Three Eigenvalues of Diffusion Tensor
  Major, Medium, Minor – l1, l2, l3 (L1,L2,L3 in FSL)
  Da = Axial Diffusivity = l1 ~ axonal degeneration
  Dr = Radial Diffusivity = (l2 + l3)/2 ~ myelination
Mean Diffusivity
  Magnitude of Diffusion
  Inversely related to tissue density
[mm2/s]
Major Medium Minor MD

## Slide 5
Diffusivity Measures
Role of Myelin
Myelinated
Unmyelinated
ADC (x 10-3 mm2/sec)
AD
RD

## Slide 6: Fractional Anisotropy
  Variance of diffusivity with direction
  Normalized between 0 and 1
  Ubiquitous measure of microstructure
  Extremely sensitive
  Low specificity

## Slide 7: Low SNR Biases DTI
SNR
Diffusivity
SNR
Diffusivity
Adapted from Pierpaoli et al.
MRM 1996
SNR = Signal to Noise Ratio

## Slide 8: DTI & SNR
SNR
FA
Adapted from Pierpaoli et al.
MRM 1996
Low SNR:
Biased FA, eigenvalues
Increase variance
Low SNR:
resolution < 1.5mm, long TE, high b-values, poor coil sensitivity

## Slide 9: Variance Across Studies - FA
Genu of Corpus Callosum
19 Published Studies (N >=8)
Std Dev: 0.1
Range: 0.36 (2004)
Reported DTI values inconsistent!

## Slide 10: DTI Histograms

## Slide 11
NORMAL
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
VASOGENIC EDEMA
CELLULAR INFILTRATION
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
H
H
O
MIXED
H
H
O
H
H
O
Caveat: Anisotropy has low specificity
DEMYELINATION
AXONAL LOSS AND GLIOSIS
Anisotropy
Courtesy AS Field

## Slide 12: Why DTI?
Diffusion is EXTREMELY SENSITIVE to tissue changes/differences at the microstructural level
  Myelination
  Axon damage/loss
  Cell Proliferation / Density
  Inflammation / Edema
  Ischemia
  WM Organization
  Development & Aging
Caveat – non-specific
Diffusion = Membrane/Barrier Spacings
a priori knowledge