## Slide 1
MP 651 Journal Club
Functional Connectivity in the Motor Cortex of Resting Human Brain Using Echo-Planar MRI
Bharat Biswal, F. Zerrin Yetkin, Victor M. Haughton, James S. Hyde
MRM 34:537~541, 1995

## Slide 2
Background Methods Results Conclusion
Physiological fluctuations in resting brain discovered by EPI MRI
A time course of signal intensities from a given pixel
Fourier transform used to show frequency components
[1] Heart rate [2] Respiratory sidebands with their harmonics
Low-frequency (<0.1 Hz) fluctuations observed. Focus of this paper!
High correlation between sensory motor cortex (hand movement) and low-frequency fluctuations within and across hemispheres
Correlation of electrical activity in the rat cerebral cortex with rCBF been reported
Frequency fluctuations are about the same as the fluctuations in human brain
Task-induced neuronal activity correlated with changes in [1] rCBF [2] blood oxygenation
Blood oxygenation sensitivity optimized in this study, although flow sensitivity remains
Fluctuations observed in the rat and in humans are of a similar nature

## Slide 3
Background Methods Results Conclusion
Study participant:
11 healthy human volunteers
  Right-handed (self-identified)
  8 M / 3 F (Age [24, 37])
  No history of head trauma / neurological disease
  No current use of medication and contradiction to MRI
Scan setting:
A standard GE 1.5T Signa clinical scanner
A home-built three-axis balanced-toque head gradient coil
A shielded end-capped quadrature transmit / receive birdcage radio frequency coil
Foam padding used to limit head movement

## Slide 4
Background Methods Results Conclusion
Scan protocol:
A single axial slice across motor cortex for each volunteer
High resolution GRASS sequence (TR = 600ms, TE = 10ms, FOV = 24cm, 256 x 256)
Several 512 EPI images obtained for functional imaging
  FOV = 24cm
  64 x 64
  TE = 40ms
Courtesy of: https://thealevelbiologist.co.uk/sensory-and-motor-areas-in-the-cortex/

## Slide 5
Data analysis:
Square wave ( ) function with 20s period for task activation
All time course signal intensity normalized between 0 and 1
P < 0.001 was used for statistical significance
~ 60 Pixels identified as belong to finger motor cortex by passing the threshold
A finite impulse-response low-pass filter applied with a cut-off frequency of 0.08Hz
60 correlation-coefficient images generated from each resting brain study
Pixels counted with passing correlation-coefficient of 0.35 (i.e., P < 0.001)
Background Methods Results Conclusion
Task design:
Rest state
Refrain any cognitive, language, or motor tasks
Task activation
Bilateral finger tapping
Tap each finger to the thumb sequentially
Without moving arms
Other controls: visual experiment
Rest
Task
20s
20s

## Slide 6
Background Methods Results Conclusion
FT
Time course of a pixel in motor cortex and its Fourier transform
Fluctuations happened at low frequency
The significance of these frequency peaks has not yet been investigated

## Slide 7
Background Methods Results Conclusion
Pixel-counting results / Correlation coefficient
L: left motor cortex R: right motor cortex O: rest of the brain
Control
Connectivity within one region or between regions in the rest study

## Slide 8
Background Methods Results Conclusion
Histograms of the distribution of correlation coefficients magnitudes
nLL and nRR
nLR and nRL
More strongly correlated pixel pairs in the task-activated data

## Slide 9
Background Methods Results Conclusion
Correlations with voxels in motor cortex at rest

## Slide 10
Background Methods Results Conclusion
Similar fluctuations giving rise to functional connectivity observed in the auditory and visual cortex
General phenomena, not due to imagined motor tasks.
Imaged activation was random for each subject as well as between subjects.
Comparisons using different reference vectors needed for further investigation.
Limitations and Future Work
Whole-volume RF coil necessary for study correlation of fluctuations across entire brain.
Surface coil can be used to obtain high quality data.
Conclusion
Functionally related brain regions showed correlation of low frequency fluctuations in resting state detected by EPI data.
Low frequency fluctuation of blood flow and oxygenation is indeed a neurophysiological index.